## Slide 1: Earth Action Highlight Coastal Sea Floor Maps from ICESat-2 will Improve Maritime Safety and Efficiency
ICESat-2’s lidar has the crucial ability to map seafloor in shallow waters globally.
ATL24, the latest bathymetry product, offers details of features as small as a few meters.
Will significantly reduce vessel groundings, potentially saving millions annually and decreasing insurance costs
Also potentially improving routing efficiency with as much as a ~7% fuel savings.
Image Credit: Christopher Parrish
Notes: Photo Story
Upper left: 78-foot sailing vessel grounded on a coral reef near Flamenco Beach, Puerto Rico in 2024.
Upper right: Accident area marked by a red X overlaid on ICESat-2 ground tracks.
Lower: ATL24 showed clear shoaling (red circle).
Highlight:
Situation/Problem. Shallow water can contain hidden hazards that cause severe damage or sink vessels. Maritime accident fatalities linked specifically to coastal hazards are not isolated in the data, but 7,604 injuries occurred from 2014–2023 in the US, with many incidents occurring in port or coastal areas. Most of the commerce for the United States comes in through shipping, approximately 90%, and those ships are required to use nautical charts. Shallow-water depth data that is recent (~30 days or faster) and accurate is needed to update the nautical charts, but there still exists many places in the U.S. and around the world, with outdated measurements or with no data at all. For example, PotashCorp-Aurora is losing $2 to $3 million a month, a siphoning of funds that has nothing to do with product demand. Instead, it’s caused by sand — specifically, excessive shoaling (the accumulation of sediment that leads to the formation of shoals, which are shallow areas in bodies of water that can pose navigational hazards) in the Beaufort Inlet channel that’s forcing ships to lighten their loads to enter the harbor.“
Solution. Before launch, ICESat-2’s Early Adopters program (known as Applied Users post-launch) built a broad user community to maximize data use and explore potential applications. Not an initial measurement requirement for the ICESat-2 mission, NASA’s ICESat-2 Early Adopters demonstrated early on the utility and benefits of using ICESat-2 satellite derived-bathymetry globally. Bathymetry is the study and measurement of the depths and shapes of underwater terrain (underwater topography). NASA’s ICESat-2 532 nm laser is ideal for underwater mapping. As a spaceborne mission it offers many opportunities to catch the coastal area at the right time (good water clarity), season and stage of tide. It also provides data globally, filling gaps in remote areas that are hard to reach and expensive to map with hydrographic surveys. Co-led by an Early Adopter, ATL24 is ICESat-2’s newest bathymetry product (released April 2025), offering unprecedented details (±0.65 m accuracy and can detect features as small as 1 m along track) of costal waters globally and detecting features as small as a few meters. ATL24 provides global along-track coastal and nearshore bathymetry, consisting of refraction-corrected seafloor and sea surface heights (orthometric and ellipsoidal heights and instantaneous depths), as well as associated uncertainties. The data are derived from ATLAS/ICESat-2 L2A Global Geolocated Photon Data (ATL03). End users include NOAA who will use it to generate reference depths for the NOAA tool, NGOs like Global Fishing watch who monitors potential fishing areas, benthic habitat monitoring, NOAA’s National Geodetic Survey or the USACE National Coastal Mapping Program, U.S. Army Corps of Engineers (USACE) to monitor nearshore coastal change
Impact/Result. NASA Early Adopters provided early examples of how ICESat-2-derived bathymetric data can be used to create real-world solutions. From saving thousands of dollars and months of work for sending hydrographic ships to an area of interest to helping engineering firms plan for real state in protected areas. Enhanced bathymetric data to accurately map the shape of the seafloor could allow for more direct routing by providing detailed information about underwater obstacles and shallow areas. This could allow navigation systems to plan routes that avoid these hazards, leading to shorter and more efficient journeys. Route optimization can reduce fuel consumption for most vessel types. Government and commercial entities can leverage this cost-effective solution to enhance maritime safety, supporting administration priorities for infrastructure safety, economic competitiveness, and coastal protection. ATL24 could significantly reduce groundings, potentially saving $B annually by decreasing insurance premiums, and improving routing efficiency with ~7% fuel savings. A 2022 study by NOAA economists estimated the overall annual value* of NOAA’s electronic navigational charts at $2 to $3.4 billion per year!​ When ATL24 is integrated into the SatBathy tool at NOAA, it would contribute to this annual value.
[1] https://www.mdpi.com/2072-4292/11/4/406
[2] Dr. Christopher Parrish (OSU; https://engineering.oregonstate.edu/people/christopher-parrish), Dr. Lori Magruder (UTexas; https://www.ae.utexas.edu/people/faculty/faculty-directory/magruder), and their team developed the ATL24 data set.
[3] https://nsidc.org/data/atl24/versions/1
[4] https://www.iims.org.uk/emsa-annual-overview-of-marine-casualties-and-incidents-2024/
[5] https://www.frontiersin.org/journals/marine-science/articles/10.3389/fmars.2019.00283/full
[6] https://www.sciencedirect.com/science/article/pii/S0029801822012239
Learn more about ATL24 during the Earthdata webinar here - https://www.youtube.com/watch?v=yX0N0ij1iQ4
More information about the data product - https://nsidc.org/data/atl24/versions/1
More info:
Early Adopters - Before launch, ICESat-2’s Early Adopters program built a broad user community to maximize data use and explore potential applications.
Applied Users - After launch, Early Adopters became the Applied Users program, which promotes applications research on integrating ICESat-2 data into organizations’ policy, business, and management activities to improve decision-making efforts.
Satellite-derived bathymetry (SDB) is the process of mapping the seafloor using satellite imagery, relating light penetration and reflection in water to estimate depths.
SDB provides several advantages, including cost-effectiveness, global coverage and faster data acquisition. SDB can be limited by water clarity, preventing light from reaching the bottom, spatial resolution of the remote sensing measurement and accuracy, depending on the method and satellite platform/instrument.
Despite its limitations, SDB can be used in a wide variety of applications, including coastal zone management, navigation and safety, marine habitat monitoring and disaster response.
ICESat-2 has become a major contributor to SDB, with over 2000 publications on this topic to date. Now is the time to think about the state-of-the-art and additional capabilities of SDB for the future.